## Slide 1
Arief Noor Rahman
Senior Power Electronic HW/Control/FW Engineer
noorrahman.arief@gmail.com
https://www.linkedin.com/in/arief-noor-rahman-3880a536
https://forum.qorvo.com/u/physicboy/summary
https://github.com/physicboy/QSPICE
PWL SiC MOSFET Transient Losses Analysis in Qspice - Rev. 0
PWL based transient losses analysis is previously popularized by PLECS and PSIM.

## Slide 2: Introduction
Losses analysis is one of the most crucial design aspect within power electronic. Improper losses analysis often lead to early overheat during prototyping stage which then require more PCB iterations and potentially extend the overall development cycle time.
There are multiple approaches engineers do to perform losses analysis. The simplest method is just using Excel based on the datasheet’s parameter. This method is reasonable for simple topology but cumbersome or nearly impossible for more complex topology. Another method could be using Spice model of the device then run Spice simulation. Unfortunately simulating switching converter with full device semiconductor model are both very slow and very prone to simulation not converging.
Another solution that is now popular is to use ideal Switch simulation in PWL based simulator (i.e. PLECS, PSIM, Simba, etc) to obtain the device voltage and current during both ON state, turn on event and turn off event. Then, use simple math to estimate the losses by interpolating the data from losses table (pre-computed or measurement). This method have the benefit of being very fast and quite good accuracy (depending on how the user generate the losses table).
Here, I emulate the similar algorithm used by these propietary software and implement them in Qspice. At this moment, I am using a simplified version of losses table due to my C-coding limitation. I hope there will be some potential contributor to further extend the performance in the future.
Rgon = Turn on gate resistance
Rgoff = Turn off gate resistance
dtime = deadtime duration
Npara = Number of parallel device
xx_factor = losses correction scaling factor
fname = losses table file name

## Slide 3: 5 kinds of power losses in SiC MOSFET
Note1: losses is calculated as an average for each switching period
Note2: In this case, we are ignoring body diode reverse recovery loss since its mostly negligible.
Conduction Loss
Turn on loss
Turn off loss
Body diode deadtime loss
Coss loss

## Slide 4: Understanding the losses table format
Rdson | Ton | Toff | Rg_test | Rg_int | 0.0
Vds (0V) |  |  |  |  | Vds (Vrating)
Coss(@Vds) |  |  |  |  | Coss(@Vds)
Isd (0A) |  |  |  |  | Isd (Irating)
Vsd(@Isd) |  |  |  |  | Vsd(@Isd)
The table size must be strictly 5x6 and written with the exact format.
Between one collumn to the next, the data is separated by using tab (tab delimited data).
The losses Eoss and body diode are calculated by taking linear interpolation from the losses table. The data table dont need to be equally spaced. If the Vds or Id is greater than the highest value in the datasheet, the Eoss and Vsd are assumed to be equal to the maximum value on the table.

## Slide 5: Reasoning for losses table design
The losses table used in this design is much simpler than the table used by PLECS. The reasoning why this table might be reasonably acceptable is because the more complex table is still a simple approximation as it only based on measurement with one gate resistance value, one or a few Vds levels, and some Id levels, and typically only measured at 25⁰C and at Tj(op),max.
Second part that might be worth a discussion is, the linear simplification of switching loss parameter into Ton and Toff. As shown below, Infineon and Rohm are very linear thus the assumption should be considered reasonable. However while Wolfspeed and ST are more wobly curve which means the assumption may not be very correct. But anyway practically speaking, just eyeball it and call it a day if you want to choose Wolfspeed or ST or calculate the losses with Infineon/Rohm device with similar Rdson as generally losses among different vendor are not too dissimilar...haha.
Note: if you cant understand the second part, means you havent work in company. Where it is common for us to simply swap MOSFET with similar Rdson from supplier A to supplier B, in most cases nothing really bad happened except with simply 5~10⁰C temp.
Rohm SCT3040KR
Wolfspeed C3M0016120D
Infineon IMW120R040M1H
ST SCT018W65G3AG

## Slide 6: Preparing the table - 1
I believe for most of the parameters are quite self explanatory.
However, for Ton and Toff, please be sure that the datasheet parameter is measured using diode clamped inductive switching test (double pulse test) instead of resistive switching test as commonly used by older silicon MOSFET datasheet.

## Slide 7: Preparing the table - 2
In case Td and Toff are still obtained using old method, user can also calculate Ton and Toff from Switching losses chart (or hardware measurement).
We can easily calculate Ton and Toff using following formula.
Please note, Eon in datasheet is often defined as total of turn on switching loss and Coss loss. The easy way to check this is by look at the base of the Eon plot and see if it converge to zero at Id = 0 or not.

## Slide 8: Testing

## Slide 9: Conclusion
An alternative method of transient loss estimation has been developed to be used in Qspice.
The presented method has a number of simplification layers, with the rationale of the approach explained. Note: some reasoning maybe technical, some maybe practical.
Simulation result accuracy after some comparison with Wolfspeed’s speedfit appears to be quite reasonable (I cant find Infineon’s losses simulator). Though overall its greatly related to the data preparation accuracy.
Nevertheless, this tool I believe is a very powerful tool for every power supply engineer.
Next? for IGBT?
[1] Infineon IMZA75R040M1H - Datasheet
[2] Infineon IMW120R040M1H - Datasheet
[3] Estimating SiC MOSFET switching losses in applications https://community.infineon.com/t5/Knowledge-Base-Articles/Estimating-SiC-MOSFET-switching-losses-in-applications/ta-p/709113
References