## Slide 1: Three Complexity Levels of PWM Implementation for Digital Controller Simulation
By: Arief Noor Rahman

## Slide 2: Background
Qspice has great improvement over its predecessor (LTspice). My favorite feature is the added support for custom digital block (C and Verilog). Which allows more efficient and more direct implementation of various control, analysis, and signal processing algorithm (instead of using circuit/behavioral source or as post processing).
This article provides a method on how to use C-block to achieve digital smps simulation as fast and as accurate as possible.
Some background information about the C-block implementation as well as my own understanding of the interaction between main Spice solver with the C-block are provided.

## Slide 3: Structure of C-block for Qspice
useful to print some statements on the Qspice console. But remember to not overuse it, because it use msleep(30) to wait so that the Qspice can fetch the print out statements. However, it also slows down the sim each time display() is called.
this union defined all the data types used for the input/output for the C-block. we can leave it as is.
this is something to do with how windows load the .dll and allow the code to be called. we can leave it as is.
upon call bzero(), it reset all the value in the struct sBUCK_X1 to zero
user can define most of all data in struct sBUCK_X1. the data defined in sBUCK_X1 will be maintained by Qspice throughout all the simulation, even when negative timestep is applied.
main function for all the algorithm implementation.
*note: things in if(!opaque){} will be executed once at the beginning of the simulation. users can put some calculation there that just need to run once.
Qspice will call this function to determine the maximum allowable time step. Qspice takes into account all suggestion from all components in the simulation
Qspice calls this function to read if there is any suggestion for the next timestep. Qspice take into account all suggestion from all components in the simulation.
This function only called once upon the termination of the simulation.

## Slide 4: Tricky Parts about C-block and Timing within Qspice
Qspice use variable timestep, furthermore upon nonlinearity event detection (i.e. transistor switching, or diode on DCM), Qspice can even apply negative timestep to ensure the exact timing of the non-linear event is properly captured. This behavior can mess up with C-block as most control/signal processing algorithm are not designed with negative timestep. Where it can cause the user’s algorithm to be called multitle time for the same simulation run time. To avoid this, ensure that the variables that is sensitive to simulation runtime must be defined within the struct sBuck_X1
Trunc() is used to provide suggestion of next timestep. The primary suggestion from the template is based on the working principle of Qspice own’s variable timestep algorithm, where if the result of the next timestep induces a nonlinearity then revert back to the minimum timestep. After trying with minimum timestep for a few steps, then next timestep is double of the current timestep. The timestep will keep increasing until max timestep is reach or nonlinearity event is detected. To speed up the simulation, in case of digital control smps, we can exploit the characteristic of the digital pwm implementation where the duty cycle for the of the future switching period is defined by the last sampling period. Means we can set send the Qspice solver the next timestep suggestion to directly hit the next transistor switching time.
  *note: Qspice takes in the smallest maxtimestep and smallest timestep suggestion from all components in the simulation schematic

## Slide 5: The three levels of complexity Level 1 : C-block only for control algorithm
In this approach, C-block only performs the control algorithm that read analog feedback and send out duty cycle command. Sampling timing control for C-block is provided by the clk (V3) and the pwm pulse output is provided by carrier (V2) and comparator (B2).
Note 1: Model definition for SWH and SWL have parameter ttol=1n to force Qspice to iterate around the exact switching event with the accuracy down to 1ns. Additionally, Qspice also conduct some iteration around the peak and valley of the carrier triangle waveform and at the rise/fall time of clk source.
Note 2: Simulation exhibit some strange unrealistic oscillation, thus the solver changed to gear which have oscillation damping behavior
Note 3: This method is the simplest, however the multiple timestep iteration around the discontinuity event can increase the total simulation time, especially for complex simulation with higher number of switches.

## Slide 6: The three levels of complexity Level 2 : C-block for control and basic pwm generation
For this implementation, the PWM generation, sampling timing, and control algorithm are all implemented in C-block. While for a more basic implementation the PWM generation and sampling timing can be designed using an actual triangle wave within C-block, in this implementation we skipped the triangle waveform and directly compute the future discontinuity event.
Benefit of this approach is reduced number of timestep iteration especially around the discontinuity.
Disadvantage is a small added complexity of computing the and implementing the future discontinuity event algorithm.
*In this design, PWM generation method follow the method used by TI C2000 MCU family.

## Slide 7: The three levels of complexity Level 3 : C-block for control and PWM with deadtime
The level 3 implementation extends the details of the implementation on level 2 further by implementing dead-time algorithm.